Inviscid Perfect Gas

2010halder -Upwinding is the most preferred numerical scheme for high-speed flow simulation. Upwind
schemes are usually categorized as either Flux Difference Splitting (FDS) or Flux Vector
Splitting (FVS). The most successful and popular approximate Riemann solver (FDS) is Roe’s method,
which is the exact solution of a linearized Riemann problem (Roe [8]). It is able to capture stationary
discontinuities with no numerical dissipation. However, at strong expansions, the Roe scheme tends to
diverge even if the entropy fix is applied. In addition, FDS scheme suffers from the so called “carbuncle
phenomenon” – a numerical instability in capturing strong shock waves in multidimensional
computations.
Other way of introducing upwind is FVS, in which the numerical flux function is divided into
positive and negative parts. Steger and Warming [9] made use of similarity transformations and the
homogeneity property of the Euler equation, in splitting the flux depending on the sign of the
eigenvalues of the flux Jacobian matrix. However, this splitting has problem around the sonic point,
and van Leer [10] proposed an alternative splitting, which gives noticeably better results.
These FVS schemes share a serious disadvantage: large dissipation on contact discontinuities and
shear layers.
A more recent effort to develop less-dissipative upwind schemes focuses on reducing the surplus
dissipation of the FVS by introducing the flavor of FDS into FVS schemes. Liou and Steffen [11]
proposed a promising scheme named Advection Upstream Splitting Method (AUSM) (Fezoui and
Stroufflet [12]) in which the cell-face advection Mach number is appropriately defined to determine the
upwind extrapolation for the convective quantities. The AUSM + (Liou [13]) is designed to be a further
improvement of AUSM, and offers further improvement in accuracy over its predecessor (AUSM) and
other popular schemes, simplicity, and easy generalization to other conservation laws.
The desire to compute flows over complex geometrical body, the widely used multi-block structured
grid approach can be used. But the automation of the blocking and grid generation process is difficult
tasks that are continually being refined. The unstructured grid can be used for this kind of problem as
well as simple geometrical problem (Venkatakrishnan [14]; Bertolazzi and Manzini [15]; Batina [16];
Jameson and Mavriplis [17]).

In the present study the two-dimensional Euler equations are solved on unstructured triangular
meshes to study the shock interactions in high Mach number flow over double-wedge excluding the
self-induced oscillations regime (Ben-Dor et al. [7]) in the shock wave flow pattern. The driving
algorithm is an upwind biased cell-cantered finite volume method. The spatial discretization involves
a naturally dissipative flux-split approach that sharply captures shockwaves.